Featuring Native Metaheuristics for Non-Permutation Flowshop Scheduling

Andrea Rossi, Michele Lanzetta

Department of Mechanical, Nuclear and Production Engineering, University of Pisa, Italy

# Abstract

The most general flowshop scheduling problem is also addressed in the literature as non-permutation flowshop. Current processors are able to cope with the (n!)m combinatorial complexity of non-permutation flowshop scheduling by metaheuristics. After briefly discussing the requirements for a manufacturing layout to be designed and modelled as non-permutation flowshop, a disjunctive graph (digraph) approach is used to build native solutions. The implementation of an Ant Colony Optimization (ACO) algorithm is described in detail and it is shown how the biologically inspired mechanisms produce eligible schedules, as opposed to most metaheuristics approaches, which improve permutation solutions. ACO algorithms are an example of native non-permutation (NNP) solutions of the flowshop scheduling problem, opening a new perspective on building purely native approaches. The proposed NNP-ACO has been assessed over existing native approaches improving most makespan upper bounds of the benchmarks from Demirkol et al. (1998).

Keywords: Manufacturing systems; Flow Line; NPFS problem; Ant Colony System (ACS); Benchmark problems

# Introduction

In a manufacturing system, parts (jobs) visit machines based on a production plan (or schedule). The scheduling problem has the purpose of optimizing resources (e.g. machines utilization, workers time etc.). A general solution is not yet available and hence heuristics and metaheuristics solutions are proposed and compared on given problem benchmarks in order to achieve better schedules and consequently economical benefits.

Scheduling solutions for a manufacturing system model are scalable in many senses: a job can be a part, the whole product or a batch; machines (or stages) can be a single operating unit, a cell, a line, or their combinations; and time is measured by non-dimensional units. Examples of flow lines include transfer lines (assembly, machining), continuous processes (steel-making, heat treatments, coatings, chemical plants), and are also available outside the manufacturing environment (logistics, computer science, services, with high capacity utilization).

## Permutation vs non-permutation

The flowshop scheduling problem occurs whenever it is necessary to schedule a set of n jobs on m machines so that each job visits all machines in the same order. In the literature there are two major types of flowshop scheduling. In a permutation flowshop (PFS) the sequence jobs visit machines (routing) is the same for all jobs, and machines process all jobs with the same sequence (or permutation). On the contrary, in a non-permutation flowshop (NPFS) all jobs visit all machines in the same sequence, but passing of jobs on machines is allowed, i.e. the sequence (or permutation) of jobs can be different on subsequent machines.

Figure 1 Solution generation according to permutation, non-permutation and native non-permutation approaches.

Figure 1 about here

The logical steps, from physical layout to model, and the algorithm selection options are outlined in Figure 1.

In job passing, a job can overtake another job while waiting in a queue to be processed by a machine. To allow job passing, buffers between machines are necessary. Buffers can be between, on board or shared among machines; they can be shared in the form of an automatic warehouse or an open space.

The optimal solution of the flow shop scheduling problem can be determined in polynomial time when m=2 (Johnson, 1954), the general form of this kind of problem is known to be NP-complete in the strong sense when m≥3 (Garey et al., 1976). Permutation flowshop has been extensively investigated in the literature, as opposed to non-permutation. A possible reason is that there are (n!)m different schedules for ordering jobs on machines in non-permutation flowshop; the number of schedules for permutation flowshop (PFS) reduces to n!

Modeling a flow line as a permutation flowshop is the only choice when job passing between machines is not allowed, like in the case of continuous lines, buffers not present, or bulky items.

In other cases, modeling a manufacturing system as a non-permutation flowshop has several benefits. Among drawbacks of permutation flowshop are:

- If buffers are not present, either the blocking or the no-wait condition should be applied to the algorithm to achieve a feasible scheduling. In the former case, a job completed on one machine may block that machine until the next downstream machine is free while in the latter the next machine must be available before a job leaves the previous one.

- Different permutations of jobs can be opportunely selected for subsequent machines removing the constraint that all the sequences must be identical. By relaxing the permutation constraint, non-permutation schedules are potentially better. Experimental evidence is also available in the literature (Liao et al., 2006), however due to the problem complexity higher computational power is necessary. Heuristics approaches are easier to implement and provide good permutation schedules for practical purposes with lower computation time and are therefore preferred by the shop-floor manager, but unfortunately, this simplicity is bought at the price of drastically inferior schedules according to Potts et al., 1991, and Tandon et al., 1991). More recently, Pugazhendhi et al. (2002), Liao et al. (2006), and Ying et al. (2010) have overcome the permutation performance proposing better results (lower upper bounds) for benchmarks in non-permutation configuration; they are currently the state-of-the art.

To deal with the complexity of the non-permutation flowshop problem, a number of approaches are available, which improve an optimal permutation schedule by changing the job sequences on machines, as shown by the arrow paths in Figure 1. Examples are the well-known NEH heuristic to find good permutation solutions, further improved by metaheuristics, like ant colony optimization (ACO), genetic algorithms (GA), Particle Swarm Optimization (PSO), and tabu search to achieve non-permutation solutions. Lin and Ying (2009) propose a hybrid simulated annealing/tabu search method where the job sequences are the same for all machines in the initial solution of their tabu search method. Pughazendi et al. (2004) propose a simple heuristic procedure to derive non-permutation schedules from a given permutation sequence, with the added complexity of sequence-dependent setups. Brucker et al. (2003) present a number of results on the non-permutation flowshop scheduling with limited capacity buffer. They propose a procedure based on state-of-the-art tabu search, where the initial solution adopted is a permutation schedule evaluated by the NEH heuristic (Nawaz et al., 1983). Jain and Meeran (2002) consider a multi-level hybrid approach for the general flowshop scheduling problem. They hybridize a scatter search and a tabu search with the neighborhood structure proposed by Nowicki and Smutnicki (1996) for the job-shop scheduling. The initial solution is found by the insertion algorithm proposed by Werner and Winkler (1995) and it is implemented on the disjunctive graph. In general, the tabu search requires starting from a good initial solution to be improved by other heuristics.

ACO has been recently considered to cope with the complexity of other flowshop scheduling systems (Arnaout et al., 2012). Formerly Stuezle (1998) and Rajendran and Ziegler (2004) have proposed respectively a Min-Max Ant System and an Ant Colony System for the permutation flowshop scheduling. Yagmahan and Yenisey (2010) consider a multi-objective makespan and flowtime criteria and propose an ant colony optimization. They also propose to create initial ant trails with an amount of pheromone that is a function of the best solution generated by the NEH heuristic by Nawaz et al. (1983). This idea has been applied by Sadjadi et al. (2008) who applied the standard ACO specifications from Bonabeau et al. (2000) except for the diversification mechanism: the initial amount of pheromone on the digraph trails is determined by the permutation solution found by the NEH heuristic. The best found permutation schedules are improved by local search in order to obtain non-permutation solutions.

## The native non-permutation approach

As opposed to all cited works, native metaheuristic approach enforces constructive schedules. Initially it builds independent initialization sequences on all machines. Next, a schedule is generated ex-novo by each ant. This prevents the algorithm performance to be influenced by other (meta)heuristics and allows an accurate performance evaluation.

Figure 2 Digraph approach for candidate list selection (inset) and building a feasible solution.

Figure 2 about here

A possible representation of the (non-permutation flowshop) scheduling problem is based on a disjunctive graph. In a disjunctive graph (Figure 2, inset), nodes represent operations, conjunctive arcs correspond to precedence constraints among the operations for the same job, disjunctive arcs conform to possible constraints among the jobs on the same machine.

We define as native non-permutation flowshop scheduling (NNPFS) an algorithm able to generate constructive solutions in O(n(m). A NNPFS algorithm directs some disjunctive arcs in order to connect all operations with only a starting and an ending arc, i.e. the graph becomes acyclic, and the related sequences of operations on machines represent a feasible schedule. The makespan Cmax is the length of the longest path between the dummy source and destination (critical path). When a disjunctive arc is directed, the ending node is inserted in the sequence of the related machine and in a tabu list, i.e. the partial schedule generated on the digraph cannot be modified anymore. As a consequence, the longest path between the dummy source and the ending node is the completion time of the operation. Generally, the constructive mechanism is implemented by the list scheduling algorithm (Giffler and Thompson 1960). Besides, initially it starts with a random selection of nodes or a type of selection driven by dispatching rules. These features make list scheduling mandatory in NNPFS.

A typical digraph framework metaheuristic is the ant colony optimization proposed by Bonabeau et al. (2000). In ACO the digraph is an internal shared memory where, in analogy with the nature, the artificial ants, following trails of pheromone, direct disjunctive arcs to connect source and destination nodes (Figure 2). Each ant of the colony directs a number of disjunctive arcs in order to make the graph acyclic and finally the ant that connects source and destination nodes with the shortest critical path (Figure 2, bottom left) is eligible to leave a pheromone amount proportional to the path length. This is a constructive way to generate a schedule where a complete solution is generated forward by a partial solution using the stigmergy of the colony, i.e. the selection of the more promising disjunctive arcs in which more amount of pheromone is laid. The main goal of ACO mechanism is to generate the optima solution by constructive schedules. The concept is similar to “divide et impera”, because the stigmergy progressively concentrates the search in a low number of very small promising regions. Differently to local search, this fact makes the algorithm intrinsically parallel.

The literature on NPFS with ACO will be discussed in chapter ‎1.3. The mechanism of the proposed native non-permutation ACO will be described in detail in chapter ‎2 based on a digraph scheme. In addition, it will be shown how a native non-permutation algorithm for the flowshop problem is designed and the performance of the proposed algorithm compared with an existing ACO (chapter ‎3).

## Literature on native approaches and ACO in NPFS

To the best of our knowledge a native ACO has been applied only by Ying and Lin (2007) that represent the problem by a disjunctive graph and use a multi-heuristic function of visibility in an ant colony system. The visibility represents the heuristic desirability, that together with the pheromone amount, drives an ant to the selection (and the direction) of disjunctive arcs of the digraph. The multi-heuristic visibility proposed by Ying and Lin is based on the best selection within a set of schedules achieved by dispatching rules. The performance is evaluated using the benchmark problems from Demirkol et al. (1998), achieving new best results (lower upper bounds) on most benchmarks considered. Their ACO improves the previous best results obtained by the shifting bottleneck heuristic by Demirkol et al and are compared with the proposed ACO. Extensive numerical research has indicated that the shifting bottleneck heuristic is extremely effective (Pinedo 1995).

## Problem Formulation

Current problem is referred as Fm|Bi=+(|Cmax using Graham’s notation, where Fm stands for flowshop with m machines, Bi=+( denotes that buffers with infinite capacity are present, allowing non-permutation schedules, and Cmax denotes the makespan minimization as the optimization criterion.

The n jobs have to be scheduled in the same order on the m machines. Each job i, i=1,..,n, is represented by a sequence of operations, Oi j; each of these has to be processed as the jth operation on the machine at the stage j, j=1,..,m, with a processing time t(Oi j).

Given a schedule S, the quantity st(Oi j) and L(Oi j) denotes, respectively, the starting and the completion time of the operation Oi j. No resource can process more than one operation at a time; finally, no operation Oi j can start until Oi (j-1), is completed or can stop after it starts.

The problem (Figure 2, inset) can be represented by a disjunctive graph DG = (N, A, Ej, WN) where N is the set of nodes (operations), A is the set of conjunctive arcs (job routing), Ej is the set of disjunctive arcs (connecting a potential pair of operations to include in the sequence of machine – or stage – j), WN is the weight on nodes (processing times, setup and transportation times etc.). The set of nodes N has (n(m) elements plus two dummy nodes: the source “0” and the destination “*”; the set of conjunctive arcs A includes [(n+1)(m)] elements; finally, Ej includes [(n-1)(n)/2] disjunctive arcs, among all the n operations to be process on machine j, and (2(n) between each operation to be process on machine j and the dummy nodes.

A feasible solution can be constructively obtained by the list scheduling. This heuristic generates a feasible solution in (m(n) steps by inserting an allowed operation in the related machine sequence at each step. An operation is included in an allowed list if it can be reached by a conjunctive arc of A from the previous operation in the job routing that is already inserted in the machine sequence. When an operation is selected by list scheduling, it is removed from the allowed list and inserted in a tabu list.

Figure 2 shows an example of how the solution can be achieved on the digraph and will be detailed in the next chapter showing the implementation of the proposed ACO. Initially, the dummy source “0” is the starting node. At the first step, all the operations which can be reached by directed arc of A are the operations which must be processes by machine 1: O11, O21 and O31 (shown in light blue). At the second step the operation O31 is selected and inserted in the sequence of machine 1 (shown in red). At the second step, the disjunctive arc (0, O31)(E1 is directed. As a consequence, O31 is replaced from the allowed list by the next operation reached from O31 by the arc of A, i.e. O32. The length 17 in bold represents the completion time of the operation O31 in the partial constructive schedule, i.e. L(O31)=st(O31)+t(O31)=17. At the third step, the disjunctive arc (0, O21)(E1 is directed and O21 is replaced from the allowed list by the next operation reached from O21 by the arc of A, i.e. O22. The completion time L(O21)=31 is evaluated by the longest path from the dummy source “0”. This path length is evaluated by adding the processing time t(O21)=31 to the maximum length between the two nodes from which the current node can be reached: respectively, O31, by the arc just directed, and the dummy “0”, by the related routing arc of A. It can be noticed that the maximum completion times between O31 and “0” is the starting time of node O32, st(O32). The algorithm runs for [(m(n)-2] more steps generating the acyclic graph of Figure 2: at the (m(n)th step all nodes will turn red and their completion time will be displayed. The makespan is evaluated from the node with the maximum path length.

# The proposed approach

This section describes an ant colony system (ACS) for the native non-permutation flowshop scheduling problem. Ant colony systems, a subset class of ACO, are an emerging class of biologically inspired research dealing with artificial or swarm intelligence: it exploits the experience of an ant colony as a model of self-organisation in co-operative food retrieval. The ant runs the nest-food path by a probabilistic selection of nodes according to the following properties:

- diversification in order to produce promising alternative paths;

- intensification to select a node in the vicinity of the current best paths.

As soon as all the paths of the ants in the colony are generated, the best ant deposits on the arc a further amount of pheromone proportional to the path length and a pheromone decay routine is performed to prevent the stagnation in local optima solutions. The pheromone trail is the basic mechanism of communication among real ants and it is mimicked by the ant colony system in order to find the shortest path connecting source and destination on a weighted graph, which represents the optimization problem.

List scheduling, which is a process guided only by the function of visibility, becomes driven also by the pheromone amount. In fact, the selection of a candidate node can be performed based on the disjunctive arc that connects it. At the start, the pheromone is randomly deposited; consequently, the node selection is random as in pure list scheduling algorithms. As epochs evolve, the deposited pheromone drives the arc selection.

The following mechanisms have been implemented in the proposed ACO and are described in detail:

- path generation, to transform the digraph in an acyclic conjunctive graph by a stochastic process based the amount of pheromone;

- candidate list construction, to select operations, not only to achieve feasible schedules, but also in order not to exceed the idle time more than a predefined value;

- local update rule, for diversification purposes;

- off-line pheromone update rule, for intensification purposes;

- local search, to better improve the best found solution.

## Digraph model

The disjunctive graph is also able to implement pheromone trails. In this case the DG = (N, A, Ej, WN, WE ) has the new component WE, which represents the weight on disjunctive arcs (pheromone amount). The weight on the disjunctive arcs (Oi’j, Oi j) of E j is represented by the pair WE(Oi’j’,Oi j) =(p[Oi’j’,  Oi j], p[Oi j, Oi’j’]). The first component array p[Oi’j’,  Oi j] gives an index of desirability in order to insert the feasible move (i.e. the sub-sequence) [Oi’j’, Oi j] in the current location of the loading sequence of resource j. The pheromone trail WE is a two-dimensional array of (m(n((n+1)) elements (considering that the number of disjunctive arcs among all the n operations to be process on machine j that can be replicated is [n (n-1)/2]). Hence, the internal shared memory of the proposed ant colony system is O(m(n2).

## Path generation

To generate a feasible schedule Sa, each ant a visits every operation on DG one and only one time in order to transform the digraph in an acyclic conjunctive graph. Path generation is a stochastic process where an ant starts from the dummy “0” and selects the next node from a subset of the allowed operations, the candidate list CL. It uses the following transition probability rule of the pheromone trail as a function of both the heuristic function of desirability, ( (the visibility function), and the amount of pheromone ( on the edge (Oi j , J), with J ( CL:

(1)

The non-negative parameters ( and ( represent the intensity of respectively, the amount of pheromone and the visibility included in the transition probability function. The non-negative parameter q0 is the cutting exploration, a mechanism that restricts the selection of the next operation from the candidate list CL. If a random number q is higher than the cutting exploration parameter q0 (0( q0(1), the candidate operation is selected examining in probability all the candidate operations which are as much desirable as higher visibility and pheromone amount are; otherwise is taken the most desirable operation, i.e. the arc with the highest amount of pheromone and the highest visibility.

The role of cutting exploration is that of explicitly split the search space in order to achieve a compromise between the probabilistic mechanism adopted for q ( q0 or the further intensification mechanism of exploring near the best path so far, which corresponds to an exploitation of the knowledge available about the problem. By tuning parameter q0 near 1, cutting exploration allows the activity of the system to concentrate on the best solutions (exploitation activity) instead of letting it explore constantly (exploration activity, achieved by tuning parameter q0 near 0). In fact, when q0 is close to 0, all the candidate solutions are examined in probability, whereas when q0  is close to 1, only the local optimal solution is selected by equation. In this paper a freezing function similar to one proposed by Kumar et al. (2003) is considered. It progressively freeze the system by tuning q0 from 0 to 1 in order to favour the exploration in the initial part of the algorithm by means of the following expression:

(2)

where epoch is the current iteration and n_epochs is the total number of iterations of the ant colony system.

The heuristic function of desirability ( is a very critical component of ant colony systems. Generally, it is implemented by dispatching rules, as in Ying and Lin (2007). A comparison among a number of dispatching rules to implement the visibility function has been performed by Blum and Sampels (2004). In this paper the earliest stating time (EST) heuristic, i.e. the best heuristic tested by Blum and Sampels (2004), is used.

## Candidate list construction

The candidate list does not include all the operations that can be selected at a given construction step of the algorithm. In fact, it is well known that the optimal schedule is always an active schedule, i.e. a feasible schedule in which no operation could be started earlier without delaying some other operations or breaking a precedence constraint. Thus, the search space can be safely limited to the set of all active schedules. An important class of active schedules is the non-delay schedule: these are schedules in which no machine is kept idle when it could start processing some operations. As no all-optimal schedules are non-delay, the concept of parameterized non-delay schedules is used. This type of schedule consists of schedules in which no machine is kept idle for more than a predefined value ( if it could start processing some operations. As the minimum starting time of a candidate operation is:

(3)

all the operations O* which can start if no machine is kept idle for more than a predefined value (, verify the following condition:

(4)

In this paper a strategy which relaxes the expression (4) is considered by using the following parametric value of ( :

(5)

where rf is the restricted factor. If the restriction is maximum, i.e. rf ( +(, the predefined value ( (rf) tends to zero and we obtain a non-delay schedule, i.e. CL=AL; on the contrary, if rf is set higher than 0, the property of non-delay schedule is relaxed; finally, if rf = 0 the candidate list does not differ from the allowed list, i.e. no restriction to AL occurs. To sum up, the following candidate list is used:

(6)

where is considered the restricted factor rf equal to 3.

## Local update rule

The local update rule is applied to favour the exploration of not visited nodes by other ants of the colony. This rule imposes to the ant that has selected a candidate operation J, of laying on the connecting arc (Oi j, J) the following negative amount of pheromone:

((Oi’j , J) = (1-() ( ((Oi’j , J) + ( ( (0	(7)

As for the off-line update rule, local update rule is a convex combinations of parameter equal to the evaporation coefficient; in this case the convex combination has points, ((Oi j , J) and (0. This causes a reduction of the pheromone amount on a selected arc, because it ranges between the previous value ((Oi j , J) and the initial value (0. As a consequence, the effect of this rule is making nodes less and less attractive as they are visited by ants, indirectly favouring the exploration of not visited nodes. This is a basic diversification mechanism because it makes the generation of alternative paths by next ants possible.

## Off-line pheromone update rule

This feature arises when a positive amount of pheromone has to be deposited. At the end of an epoch, in order to make more directed the exploration of the best nest-food path by the entire colony, the ant which detects the best path in the epoch, termed best-epoch ant (Sbe) performs an off-line update rule of pheromone. This rule consists in to deposits on the acyclic graph generated by Sbe a further amount of pheromone, proportional to the following convex combinations of points ( (Oi j r, J) and makespan(Sbe)-1, making possible an intensification of the search in the vicinity of the best solution by the other ants of the colony:

((Oi j , J) = (1-( )( ( (Oi j , J) + ( ( makespan(Sbe) -1,         (Oi j , J)( Sbe	(8)

= (1-( )( ( (Oi j , J),          otherwise

The amount of pheromone which remains on the selected edge ranges between the previous value, ( (Oi j , J), and a more close value to the optimum: makespan(Sbe)-1 . On the contrary, a routine of pheromone decay on the pheromone trails is performed on the other arcs of the digraph, thus indicating that a path rarely used probably does not lead to optimal solutions.

## Local search

When a path is generated, the solution is taken to its local optimum by a local search routine. The mechanism considered is a steepest descent algorithm where, at each iteration, the current best solution is replaced with an improving solution included in the neighbour of current best. The performance of the local search depends on the neighbourhood structure, which can be derived from the state-of-art local search for job-shop scheduling. In this paper, the neighbourhood structure proposed by Nowicki and Smutnicki (1996) for their fast tabu search algorithm is adopted.

## Stability condition

The stop criterion is sometimes a fixed epoch number or computation time. Instead, we use a stability condition, corresponding to a fixed number of epochs (3000), with error reduction of at least one processing time unit per epoch to stop the algorithm.

## ACS implementation

The following pseudo-code gives a high-level description of a general ant colony system for flowshop scheduling.

Algorithm. High-level description of Ant Colony System for Native Non-Permutation Flowshop Scheduling

Input: a weighted digraph WDG=(N, A, Ej, WN, WE)

// Initialization

for each disjunctive arc (Oi’j’,Oij) of EA deposit a small constant amount of pheromone WE(Oi’j’,Oij) =(0, 0) where

epoch ( 1; not_improve( 0;

// Main Loop

while (not_improve < stability_condition) do

// Epoch Loop

for each ant a, a=1 to ps do

// Path Generation

Sa  ;

- O  Oi j i=1,..,n, j=1,..,m;

- Inizialization of Candidate Nodes: AL1  Oi j i=1,..,n, j=1;

for each w =1 to n(m do

- Restriction: restrict ALw to the candidate list CLw by means of the expression (6);

- Inizialization of Feasible Moves (i.e. the disjunctive arcs connected to operation of CLw);

- Move Selection: select a feasible move (Oi’j , Oi j) of Ej, where Oi j (CL, by means of the transition probability rules (1); directing the related disjunctive arc (Oi’j  =‘dummy 0’,if j =1);

- Arc Removing: remove all the disjunctive connected to Oi’j (i.e. no other operation can be immediately subsequent to Oi’j in the machine sequence);

- Path length evaluation: the length L(Oi j) of the longest path which connects Oi j to the dummy “0” is evaluated by L(Oi j) = t(Oi j)+max (L(Oi’j), L(O(i-1) j)(  and it is placed as a mark near to the scheduled operation;

- Local Updating: apply the local update rule (8) to the arcs (Oi’j, Oi j) ( WE;

- Update Allowed List: remove the scheduled operation to the allowed list,

ALw ALw ( Oi (j+1) Oi j if j ( m-1;

ALw / Oi j otherwise;

end for

10.  Directing the remaining disjunctive arcs(these arcs are connected to dummy ’*’)

11.  Local Search: Apply local search with neighbour structure of Nowicki and Smutnicki (1996) to Sa;

12.  Best Evaluation: if (makespan(Sa)<makespan(Sbe))

then (makespan(Sbe) makespan(Sa) and Sbe Sa )

end if

end for

Global Updating: Apply the global update rule (5);

Best Ant Evaluation: if (makespan(Sbe)<makespan(S*))

then ((makespan(S*)  makespan(Sbe); S* Sbe and epoch0) and

not_improve ( 0;

else  epoch ++ and not_improve ++;

end if

end while

Output: S*

The main parameters of the two ACO approaches are also listed in Table 1.

Table 1 Tested parameters for the ant colony systems under comparison from Ying and Lin (2007) and from the proposed NNP-ACS.

| Parameter | MHD-ACS | NNP-ACS |
| --- | --- | --- |
| Population size | 5, 10, 20, 50, 100 | 5, 6, 7, 8 |
| ( | (0.1 + 0.2 ( i), i=1,…,5 | 0.1, 0.2, 0.5, 1, 1.5, 2 |
| ( | 0.1, 0.5, 1, 2, 5 | (0.04 ( i), i=1,…,9 |
| q0 | (0.1 + 0.2 ( i), i=1,…,5 |  |
| ( | (0.1 + 0.2 ( i), i=1,…,5 | (0.1 ( i), i=1,…,8 |
| Visibility function | MHD | EST, PAST (Rossi and Dini 2007) |

# Computation experiments

The effectiveness of the proposed heuristic has been verified by performing computational experiments on well-known benchmark problems from Demirkol et al. (1998), for comparison with other approaches using an identical test set.

Benchmarks are arrays bn(m. The n(m operations of each job on all machines are represented by sequences of their processing times. Each benchmark instance k includes a lower (LB n m k) and upper bound (UB n m k). The lower (upper) bound is the maximum (minimum) known theoretical minimum (maximum) attainable target optimization parameter, in this case the makespan Cmax. The upper bound can be reduced by improved solutions. If it coincides with the lower bound, the global optima solution has been reached.

Metrics for algorithm performance are the %gap from the lower and upper bounds of benchmark instances bn(m of the original dataset and from other researchers:

(9)

The proposed Native Non Permutation Ant Colony Optimization (NNP-ACS) is compared with the Shifting Bottleneck DMU-SB from Demirkol et al. (1998) and the Multiheuristic Desirability Ant Colony System MHD-ACS from Ying and Lin (2007).

The test problem set adopted herein was established by Demirkol, Mehta, and Uzsoy (DMU) and includes 40 test instances, generated as follows. All jobs are available at time zero, and the operation processing times are generated by a discrete uniform distribution between 1 and 200.

Four job number values n=20, 30, 40 and 50 and two machine number values m=15 and 20 result in eight combinations of m and n and a total number of operations ranging from 300 to 1000.

The ratio of n to m varies between 1 and 3.3. These combinations yield a problem set that is not based on a specific application. Ten instances were generated for each of the eight combinations of m and n. Since the size and complexity of the instances make exact solutions impractical, Demirkol et al. solved each instance by five different constructive heuristics and three versions of the shifting bottleneck procedure. All algorithms were run on a SUN SPARC® server 1000 Model 1104 with a 50 MHz processor, which is a multitasking system running under Unix®. The upper bound (UB) for each instance was the best solution found by any of the algorithms.

The best available solutions for the test problem set in the literature appear to be those proposed by Demirkol et al. (1998). A lower bound (LB) can be obtained for each instance by relaxing the capacity constraints on all but one machine and solving to optimality the resulting single machine problem of minimizing makespan with release and delivery times (Demirkol et al., 1998). Demirkol et al. performed this method for each machine, and reported the highest makespan value obtained as a lower bound in each instance. To obtain a more compact and challenging set of test problems, Demirkol et al. ranked the instances according to decreasing order of percentage gap between the upper and lower bounds for each combination of m and n. Only the first five instances for each combination were finally presented. Thus, a total of 40 test instances were obtained as listed in the first three columns of Table 3 and denoted by the term flcmax_n_m_k.

The other columns in Table 3 list the makespan obtained with the MHD and the proposed ant colony system with their processing times.

Figure 3 %gap of tested algorithms on benchmark problems.

Figure 3 about here

The %gap defined in (9) for the original dataset is graphically shown by the diamonds in Figure 3 and ranges between 32 and 18%. The periodic behaviour is related to the increasing benchmark size (increasing machine number and job number), and to the decreasing difficulty according to which they are sorted. It can be noticed that the difficulty of subsets of 5 benchmarks of size n(m is not monotonic, e.g. for n=20 and 30 the %gap slightly decreases from m=15 to 20 (32-25% to 28-23% and 30-23% to 29-22%). For n=40 they are similar (26-22% to 26-20%). Only for n=50 the %gap increases from 15 to 20 machines (22-19% to 31-24%).

The best makespan of 5 runs of the MHD-ACS algorithm and corresponding time are listed for comparison within the same class of native non-permutation in Table 3.

The proposed NNP-ACS has been run 10 times with the parameters in Table 3 on 3 GHz 32 bit Intel® Pentium® IV based PCs with 2 GB RAM. The average and the best solutions along with its corresponding time have been reported in Table 3. A scale factor of two, based on the speed of PC processor used by respective authors, can be applied to the processing time for comparison with the MHD-ACS algorithm.

Table 2 Selected non-optimal parameters for the ant colony system in Ying and Lin (2007) and the proposed NNP-ACS.

| Parameter | MHD-ACS | NNP-ACS |
| --- | --- | --- |
| Population size | 5 | 8 |
| (0 |  |  |
| ( | 0.1 | 2 |
| ( | 2 | 0.3 |
| Epoch number | 5000 | not_improve < stability_condition |
| stability_condition | NA | 3000 |
| q0 | 0.9 |  |
| ( | 0.1 | 0.12 |
| Local search | NA | steepest descent (Nowicki and Smutnicki, 1996) |
| Visibility function | MHD | EST |
| Candidate list | NA |  |

# Results

Table 3 also lists the results of the state of the art ant colony system algorithm and those achieved with the described ant colony system.

The new upper bounds for the three native approaches are shown in bold. For 35 of the 40 benchmarks examined new upper bounds have been found. The only original upper bounds from Demirkol et al., which have not been met, are flcmax_30_20_2 and flcmax_50_20_4.

On average, the %gap from LB before current work was 24.22 and has been lowered now to 21.01%, showing room for further improvements and research.

Figure 3 shows the performance of the three native non-permutation algorithms under comparison with respect to the LB.

Table 3 Benchmark problems, state of the art solutions and results of computation experiments.

| Algorithm ( | Bench-mark | DMU-SB | MHD-ACS | NNP-ACS |
| --- | --- | --- | --- | --- |
| Instance ( | LB | Cbest | Cbest | Time [s] | Cbest | Time [s] | Cavg |
| flcmax_20_15_3 | 3354 | 4437 | 4420 | 46 | 4047 | 330 | 4113.4 |
| flcmax_20_15_6 | 3168 | 4144 | 4044 | 46 | 3950 | 36 | 3977.5 |
| flcmax_20_15_4 | 2997 | 3779 | 3786 | 46 | 3692 | 114 | 3730.6 |
| flcmax_20_15_10 | 3420 | 4302 | 4265 | 45 | 4176 | 96 | 4221.7 |
| flcmax_20_15_5 | 3494 | 4373 | 4310 | 45 | 4097 | 66 | 4124.9 |
| flcmax_20_20_1 | 3776 | 4821 | 4819 | 59 | 4790 | 30 | 4826.9 |
| flcmax_20_20_3 | 3758 | 4779 | 4723 | 60 | 4694 | 114 | 4715.7 |
| flcmax_20_20_9 | 3902 | 4944 | 4922 | 60 | 4720 | 282 | 4775.4 |
| flcmax_20_20_2 | 3881 | 4886 | 4847 | 60 | 4731 | 282 | 4781.3 |
| flcmax_20_20_10 | 3823 | 4717 | 4715 | 60 | 4554 | 24 | 4607.6 |
| flcmax_30_15_3 | 4020 | 5226 | 5210 | 93 | 4927 | 438 | 5032.2 |
| flcmax_30_15_4 | 4080 | 5304 | 5284 | 94 | 5033 | 78 | 5092.4 |
| flcmax_30_15_9 | 4022 | 5079 | 5075 | 95 | 4912 | 114 | 4968.6 |
| flcmax_30_15_8 | 4490 | 5605 | 5593 | 94 | 5220 | 42 | 5320.2 |
| flcmax_30_15_6 | 4184 | 5147 | 5149 | 93 | 5097 | 456 | 5158.5 |
| flcmax_30_20_3 | 4806 | 6183 | 5987 | 121 | 5794 | 84 | 5846.9 |
| flcmax_30_20_1 | 4772 | 6037 | 5989 | 124 | 6179 | 126 | 6221.8 |
| flcmax_30_20_6 | 5004 | 6241 | 6195 | 124 | 6039 | 84 | 6133.9 |
| flcmax_30_20_10 | 4899 | 6095 | 5923 | 121 | 5888 | 54 | 5967.7 |
| flcmax_30_20_2 | 4757 | 5822 | 5840 | 123 | 5842 | 798 | 5886.1 |
| flcmax_40_15_5 | 5560 | 6986 | 6972 | 154 | 6521 | 180 | 6594.1 |
| flcmax_40_15_9 | 5119 | 6351 | 6310 | 154 | 6244 | 354 | 6303.3 |
| flcmax_40_15_2 | 5290 | 6506 | 6532 | 154 | 6302 | 78 | 6395.6 |
| flcmax_40_15_10 | 5596 | 6845 | 6712 | 156 | 6413 | 1260 | 6445.2 |
| flcmax_40_15_8 | 5576 | 6783 | 6771 | 156 | 6526 | 294 | 6611.7 |
| flcmax_40_20_3 | 5693 | 7154 | 7132 | 210 | 7208 | 6 | 7274.5 |
| flcmax_40_20_9 | 5998 | 7528 | 7496 | 208 | 7388 | 2262 | 7484.7 |
| flcmax_40_20_6 | 5990 | 7469 | 7476 | 209 | 7455 | 936 | 7553.1 |
| flcmax_40_20_7 | 6170 | 7608 | 7588 | 207 | 7405 | 1314 | 7473.5 |
| flcmax_40_20_5 | 6011 | 7219 | 7217 | 210 | 7326 | 1614 | 7399.4 |
| flcmax_50_15_6 | 6290 | 7673 | 7631 | 238 | 7559 | 120 | 7606.8 |
| flcmax_50_15_5 | 6355 | 7679 | 7496 | 240 | 7317 | 2916 | 7368.4 |
| flcmax_50_15_1 | 6198 | 7416 | 7402 | 240 | 7205 | 1266 | 7303.8 |
| flcmax_50_15_8 | 6312 | 7548 | 7558 | 237 | 7348 | 318 | 7468.7 |
| flcmax_50_15_2 | 6531 | 7750 | 7712 | 236 | 7547 | 762 | 7644.8 |
| flcmax_50_20_2 | 6740 | 8838 | 8836 | 312 | 8436 | 738 | 8684.4 |
| flcmax_50_20_1 | 6736 | 8539 | 8521 | 312 | 8064 | 2442 | 8189.7 |
| flcmax_50_20_7 | 6756 | 8417 | 8425 | 313 | 8370 | 1470 | 8526 |
| flcmax_50_20_8 | 6897 | 8590 | 8536 | 313 | 8430 | 6024 | 8509.2 |
| flcmax_50_20_4 | 6830 | 8493 | 8502 | 312 | 8538 | 2472 | 8625.1 |

The results found are between 14.6 (flcmax_40_15_10) and 29.5 (flcmax_30_20_1) above the LB and performance are uniformly distributed in the benchmark size range from small to high.

The best makespan of the proposed algorithm is between 3.2% above (flcmax_30_20_1) to 8.4% below (flcmax_20_15_3) the best results from MHD and in 37 of 40 benchmarks, the best makespan found is lower. Similarly it is 2.4% above (flcmax_30_20_1) to 8.8 below (flcmax_20_15_3) the UB from Demirkol et al.; the best makespan found is lower in 38 of 40 benchmarks.

# Discussion

The algorithm features discussed in the ant colony system description and outlined in Table 1, have shown to positively improve the performance of the proposed algorithm.

The average makespan of the proposed ACO is lower than the best MHD solution on 31 out of 40 cases.

By watching the %gap pattern in Figure 3 it can also been observed that the proposed ACO is less dependent on the benchmark size. This may be a consequence of the stability condition.

The stability condition applied has the expected benefit of finding better solutions, by additional iterations while there are improvements, and consequently to improve the repeatability of the algorithm on different runs. This benefit has been experimentally found. The standard deviation versus the average of the makespan obtained in the 10 runs ranges from 0.29% for flcmax_40_15_10 to 1.73% for flcmax_50_20_7.

The main drawback of the stability condition is that the processing time increases and can vary significantly.

No correlation has been found between processing time and %gap from UB or LB, so the better results do not seem a consequence of the higher processing time.

# Conclusion

Increasingly good solutions are already available in the literature, also for the non-permutation flowshop problem, which take advantage of the computational power of metaheuristics. In this paper we have defined and described how to build a native non-permutation algorithm and shown how ACO fulfils this requirement: by pheromone based list scheduling on a digraph, selection of nodes from the candidate list which restricts the size of operations allowed, in addition to random initialization of pheromone.

The proposed ant colony system has been described in detail showing the differences over existing non-permutations approaches. The better performance have been assessed versus the FS benchmark from Demirkol and become the new state of the art native non-permutations algorithm.

The main strengths of the proposed ACO are: i) the intrinsic feature of a native algorithm which handles with constructive schedules using the sole stigmergy of the colony, implicitly tackling an amount of time due to the massive use of local search routines; ii) the suitable trade-off of the ( and ( parameters which strongly reduces the number of ants of the colony (ps=8); iii) the computational efficiency induced by a low colony size where each ant visits the digraph with minimum computational time, O(m(n); iv) the effective mechanism to generate the candidate list based on a parameterization of the non-delay schedules; v) the use of the freezing condition in the ant path generation which favor exploration in the initial part of the algorithm and then favor the exploitation activity instead of letting it explore constantly; vi) the use of the stability condition which improves the repeatability of the algorithm on different runs, although increasing the processing time; vii) the relative independence on the benchmark size (job and machine number).

Other metaheuristics can be designed to tackle the non-permutation flowshop problem, by taking advantage of the digraph approach discussed in this paper. Further research is required to extend the described approach to integrate other flowshop features, such as parallel machines, lot sizing for batching machines etc.

# References

Arnaout, J.-P., Musa, R., & Rabadi, G. (2012) A two-stage Ant Colony optimization algorithm to minimize the makespan on unrelated parallel machines—part II: enhancements and experimentations, J Intell Manuf, DOI 10.1007/s10845-012-0672-3.

Blum C. and Sampels M. (2004) An Ant Colony Optimization Algorithm for Shop Scheduling Problem. Journal of Mathematical Modelling and Algorithms, 3, 285-308.

Bonabeau. E., Dorigo, M., & Theraulaz, G. (2000) Inspiration for optimization from social insect behaviour. Nature, 406, 39–42.

Brucker, P., Heitmann, S., & Hurink, J. (2003) Flow-shop problems with intermediate buffers. OR Spectrum, 25, 549–574.

C.J. Liao, L.M. Liao, & C.T. Tseng (2006) A performance evaluation of permutation vs. non-permutation schedules in a flowshop, International Journal of Production Research, 44 4297–4309.

Demirkol, E., Mehta, S., & Uzsoy, R. (1998) Benchmarks for shop scheduling problems, European Journal of Operational Research, 109, 137–141.

Garey, M.R., Johnson, D.S. & Sethi, R. (1976) The complexity of flowshop and jobshop scheduling. Mathematics of Operations Research, 1 (2), 117–129.

Giffler, D., & Thompson, G.L. (1960) Algorithms for solving production scheduling problems. Oper Res, 8, 487–503.

Jain, A.S., & Meeran, S. (2002) A multi-level hybrid framework applied to the general flow-shop scheduling problem, Computers & Operations Research, 29, 1873–1901.

Johnson, S. (1954) Optimal two- and three-stage production schedules with setup times included, Naval Research Logistics Quarterly, 1, 61.

Kumar, R., Tiwari, M.K., Shankar, R. (2003) Scheduling of flexible manufacturing system: an ant colony optimization approach. J Eng Manuf, Part B, 217, 1443–53.

Lin, S.-W. & Ying, K.-C. (2009) Applying a hybrid simulated annealing and tabu search approach to non-permutation flowshop scheduling problems, International Journal of Production Research, 47 (5), 1411-1424. http://dx.doi.org/10.1080/00207540701484939.

Nawaz, M., Enscore Jr., E.E., & Ham, I. (1983) A heuristic algorithm for the m-machine, n-job flow-shop sequencing problem. OMEGA, The International Journal of Management Science, 11 (1), 91–95.

Nowicki, E., & Smutnicki, C. (1996) A fast taboo search algorithm for the job-shop problem. Management Science, 42 (6), 797–813.

Pinedo M (1995) Scheduling: theory, algorithms and system. Prentice-Hall, New Jersey.

Potts, C.N., Shmoys, D.B., & Williamson, D.P. (1991) Permutation vs. non-permutation flow shop schedules. Operations Research Letters 10, 281–284.

Pugazhendhi, S., Thiagarajan, S., Rajendran, C. & Anantharaman, N. (2004). Generating non-permutation schedules in flowlinebased manufacturing systems with sequence-dependent setup times of jobs: A heuristic approach. The International Journal of Advanced Manufacturing Technology, 23, 64–78.

Pugazhendhi, S., Thiagarajan, S., Rajendran, C., & Anantharaman, N. (2002) Performance enhancement by using non-permutation schedules in flowline-based manufacturing systems. Computers and Industrial Engineering, 44 (1), 133–57.

Rajendran, C., & Ziegler, H. (2004) Ant-colony algorithms for permutation flowshop scheduling to minimize makespan/total flowtime of jobs. European Journal of Operational Research, 155, 426–38.

Rossi A, Dini G. (2007) Flexible job-shop scheduling with routing flexibility and separable setup time using ant colony optimisation method. Robot Comput Integr Manuf, 23, 503–16.

Sadjadi, S.J., Bouquard, J.L., & Ziaee, M. (2008) An ant colony algorithm for the flowshop scheduling problem, Journal of Applied Sciences, 8 (21), 3938-44, ISSN: 1812-5654; DOI: 10.3923/jas.2008.3938.3944.

Stuetzle, T. (1998) An ant approach to the flow shop problem. Proceedings of the Sixth European Congress on Intelligent Techniques and Soft Computing (EUFIT’98), vol. 3. Verlag Mainz, Wissenschaftsverlag, Aachen, Germany, 1560–1564.

Tandon, M., Cummings, P.T., & LeVan, M.D. (1991) Flowshop sequencing with non-permutation schedules. Computers and Industrial Engineering, 15 (8), 601–607.

Werner, F., & Winkler, A. (1995) Insertion techniques for the heuristic solution of the job-shop problem. Discrete Applied Mathematics, 58 (2), 191–211.

Yagmahan, B. & Yenisey, M.M. (2010) A multi-objective ant colony system algorithm for flow shop scheduling problem, Expert Systems with Applications, 37, 1361–1368.

Ying, K.-C., & Lin, S.-W. (2007) Multi-heuristic desirability ant colony system heuristic for non-permutation flowshop scheduling problems, International Journal of Advanced Manufacturing Technology, 33, 793–802.

Ying, K.-C., Gupta, J. N.D., Lin, S.-W., & Lee, Z.-J. (2010) Permutation and non-permutation schedules for the flowline manufacturing cell with sequence dependent family setups, International Journal of Production Research, 48 (8), 2169–2184.